## Slide 1
IoT · REINFORCEMENT LEARNING · CLOUD SECURITY
Grid IoT RL
Reinforcement Learning for Real-Time Power Grid Voltage Control
Himanshu Shimpi
Edge → Cloud → AI → Action, closed in under a second
EDGE
IoT CORE
AI AGENT
ACTION

## Slide 2
MOTIVATION
Grid Faults Don't Wait for Humans to React
Voltage sags, overcurrent, frequency drift and overheating can cascade into equipment damage or outages within seconds.
Traditional monitoring relies on static thresholds and manual operator response — too slow for a modern, sensor-dense grid.
This project replaces that reactive loop with an autonomous agent that senses, decides, and acts in real time.
Traditional
Static thresholds
Manual operator response
Minutes to react
Purely reactive
This Project
Learned decision policy
Fully autonomous agent
Sub-second reaction
Adapts to patterns
VS
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
01 / 13

## Slide 3
SYSTEM DESIGN
End-to-End Architecture
Edge
Device
sensor stream
AWS
IoT Core
secure MQTT ingest
AWS
Lambda
security + orchestration
SageMaker
RL Agent
DQN inference
Device
Shadow
decision delivered
S3 Data Lake
every reading archived
SNS Alerts
fault → email notification
the RL agent's action is delivered back to the edge device via the shadow, closing the loop
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
02 / 13

## Slide 4
INPUT SIGNALS
What the Grid Tells Us, Every Second
Voltage
400–430 V
Current
60–100 A
Frequency
49.9–50.1 Hz
Temperature
30–55 °C
Power Factor
0.90–0.99
A fault is simply one or more of these signals drifting outside its normal band.
Voltage Sag
< 395 V
Voltage Swell
> 435 V
Overcurrent
> 115 A
Frequency Drop
< 49.5 Hz
Overtemp
> 65 °C
Low Power Factor
< 0.85
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
03 / 13

## Slide 5
THE DECISION-MAKER
Deep Q-Network (DQN)
5
inputs
128
hidden
64
hidden
5
actions
5 → 128 → 64 → 5, ReLU activations
FIVE POSSIBLE ACTIONS
0
No Action
1
Shed Load
2
Switch Backup
3
Reduce Generation
4
Alert Operator
Trained on 500 episodes × 1,000 steps — 500,000 simulated grid readings
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
04 / 13

## Slide 6
TRAINING SIGNAL
Teaching Good Judgment
Rewarded
Correct action taken during a real fault
Staying idle when the grid is healthy
Voltage & frequency held in the normal band
Penalized
Wrong intervention for the fault present
Ignoring a real fault entirely
Unnecessary action on a healthy grid
The agent isn't told the rules — it discovers them by trial and error across 500,000 readings.
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
05 / 13

## Slide 7
SECURITY BY DESIGN
Built Like Real Industrial IoT
mTLS
X.509 certificates per device — mutual authentication on every connection
HMAC-SHA256
Every payload is signed; tampering is detected instantly
Replay Protection
Sequence number + nonce + timestamp reject re-sent messages
Input Validation
Bounds-checked readings, rate-limited per device
VPC Isolation
Inference logic runs in a private subnet, no public exposure
Secrets Manager
Shared secrets never live in source code
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
06 / 13

## Slide 8
INFRASTRUCTURE AS CODE
Fully Automated on AWS, via Terraform
IoT Core
Lambda
SageMaker
S3
SNS
Secrets Manager
CloudWatch
VPC + IAM
One command — terraform apply — provisions the entire stack: networking, device identities, the inference pipeline, storage, alerting, and monitoring.
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
07 / 13

## Slide 9
VALIDATION
Stress-Tested Before Trusting It
Happy
Clean data, ideal network
Noisy
Sensor drift & Gaussian noise
Network
Latency, packet loss, disconnects
Attack
Replay, tampering, false data, DoS
Chaos
Everything, simultaneously
A simulated edge device runs each scenario end-to-end against the live pipeline — the same code path a real substation sensor would use.
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
08 / 13

## Slide 10
ENGINEERING DEPTH
What Real-World Deployment Teaches You
Networking is directional
A security group can allow outbound traffic yet still silently block the return path — the system just hangs, with no error.
Statelessness has limits
In-memory protections (like replay checks) reset on every restart; production systems need durable, shared state.
Config drift is a real risk
The same value hardcoded in two places will eventually disagree — infrastructure should be the single source of truth.
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
09 / 13

## Slide 11
IT WORKS
Closed Loop, End to End
Voltage sags
to 360 V
RL Agent
decides
switch_backup
94% confidence
Shadow updated
~700 ms later
From sensor reading to corrective action — fully autonomous, sub-second, and logged for audit.
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
10 / 13

## Slide 12
LOOKING AHEAD
Where This Goes Next
Durable, shared replay protection (DynamoDB) for true multi-instance safety
Live operator dashboard for real-time grid visibility
Multi-region deployment for geographic redundancy
Continual / online learning as new fault patterns emerge
Expanded fault taxonomy beyond the current six conditions
GRID IoT RL · Reinforcement Learning for Power Grid Voltage Control
11 / 13

## Slide 13
Thank You
Questions?
Himanshu Shimpi · Grid IoT RL